OUTLINE
- What is the QDX? Why is it interesting?
- What is different about QDX?
- Generation of FT8 signal
- “Normal” generation of SSB signal
- Key insight of digital radio signals
- QDX transmitter section
- QDX receive section

---
What is QDX?
- What is the QDX?
  - 5 W digital transceiver
    - 4 bands – 80,40,30,20 or
    - Handles many, but not all digital modes
  - Small size
  - Innovative architecture
    - Both receive and transmit
  - No IQ processing in PC, all done on QDX

---
QDX block diagram

---
FT8 signal
- [Call1] [Call2] [Grid square/signal report]
- Call sign 28 bits
- Grid/Signal report 15 bits
- Add FEC code bits (LDPC (174,91) code) + sync bits
  - Alltogether 174 bits to be send/decoded
- Send each 3 bit portion as one of 8 audio tones
  - Approximately 12.6 seconds transmit, 2.4 seconds decode

---
Key insight
At any given time, only one frequency is being transmitted

---
“Normal Superhet” transmitter
Fig 13.12 — Block diagram of a heterodyne filter-type SSB transmitter for multiple frequency operation.
Fig 13.12 — Block diagram of a heterodyne filter-type SSB transmitter for multiple frequency operation.

---
QDX innovation
- Since only one frequency needs to be transmitted at any time, don’t need complex “normal” ssb transmittter.
- ‘Simple oscillator, amplifier is enough
  - Provided the oscillator can be shifted by a few Hz as each new frequency is needed.
- No suppressed carrier, No supressed sideband
  - Only the one frequency to be transmitted
- Si5351 can be programmed to sub-Hz resolution at ham HF frequencies.
  - Frequency = Dial setting + “FT8 base” + 1 or 8 tone freq

---
QDX transmit chain
Class D final
90 degree phase shift

---
QDX Receive chain - 1

---
QDX receive chain 2

---
QDX controller
- STM32F401 microcontroller
  - Built in USB, audio
  - Handles communication with computer
  - Converts received audio from ADC to USB-sound format and sends to computer
  - Computes frequency of Si5351 for transmit from audio signal input
    - Zero crossing determines audio frequency
      - Frequency from computer = FT8Base + current encoded frequency
  - Selects bandpass filter

---
Conclusion
- QDX represents new way to generate digital signals
- Simpler architecture than conventional SSB generation
- Ideal rig for portable operation – small, low power needs
- Thanks for listening