Creating A Calibrated Noise Monitoring Antenna
& Using To Measure Baseline @ EOC Construction Site
Gordon Gibby KX4Z
February 2024
TECHCON 2024

---
Industry uses dBuV/m (E-Field)
Reporting the E-Field makes the measurements independent of the type of antenna or gain.
“S-Units” quite unreliable.
Spectrum analyzer dBm only useful if same antenna.
Calibrated antennas much more useful.

---
Commercial Calibrated EMC Antenna
- Industry uses Vertical monopole, high impedance amp
- $3000 used.
- Calibrated with Antenna Factor, allows conversion from Spectrum Analyzer dBm directly to dBuV/m

---
- Standards usually refer to a VERTICAL monopole….
- But our EOC / inter-county communications are generally NVIS type comms, so I have used HORIZONTAL measurements to be more applicable to the real situation.

---
Conversion
- Assumption of 50 ohm environment
- Spectrum analyzer reports POWER in dBm
- Converting to a voltage involves some squares & math
- E dBmV/m =	107dB + dBm + AF (dB) (Eq. 1)
- Universally agreed upon conversion.

---
My Procedure to Calibrate
New Antenna
- Measure likely isotropic noise with antenna whose AF can be known, calculate dBuV/m
- Measure with antenna to be calibrated, get dBm on analyzer
  - Issue: not exactly in the same “field”: full size stretched tree to tree; test antenna out on porch roof….
- Reverse the math to figure out AF for test antenna.

---
Antenna Factor for Full Size Dipole
Electromagnetic Theory allows obtaining the AF for a full sized dipole Noise (excluding point source nearby) has advantage of generally isotropic in azimuthal directions. .

---
Conversion to dBuV/m
Spectrum analyzer power measurements were then converted to E-field signal strength (dBmV/m) using Equation 1, which is derived from Ohm's Law in a 50 ohm system using the definitions of decibel for power and voltage as appropriate.
E dBmV/m =	107dB + dBm + AF (dB)	(Equation 1)
where dBm is the power measured by the spectrum analyzer.
REF: A. H. Systems, Inc. "Useful Formulas for RF Related Conversions" [Online]. Available: https://www.ahsystems.com/EMC-formulas-equations/RFconversions.php Accessed 2/10/2024.

---
Noise = Noise
- Whether measured by a full sized antenna or by a small 2-foot portable measurement antenna...the E-field of isotropic background noise is the same.
- Allows for an equality equation that gives us the Antenna Factor for the small 2-foot antenna.

---
Resulting Calibration Curve
Simple 2-foot Antenna

---
AF values at 7MHz/10MHz Suspect
- During calibration, 2-foot antenna placed on porch roof limited by 10-foot coax.
- May have been in higher noise field than comparison 100-foot dipole stretched in back yard.
- Would result in inappropriately negative AF calibration results…..
- 3.5 MHz value may be reliable, and this by itself allows useful measurement of noise environment due to harmonics of 60Hz power systems...

---
Utilization for EOC Measurement
- Alachua County, Florida is moving their EOC and Fire-Rescue Headquarters to a huge old WWII building
- Building will be renovated.
- Previous EOC beset with mega-dB RFI HASH presumably from backup power systems
- Desire to avoid repeat.

---
Monitoring Setups

---
MUST have quiet power supply!
(Embarrassing record of mea culpa.)

---
Sleuthing
- Discovered when comparing measurements back home, powered by diesel generator (free wheeling alternating controlled only by mechanical governor) versus the filtered inverter
- Utility power is also usually quiet.

---
Had to repeat entire measurement...
- Back to the site
- Utilized diesel generator
- PLUS MIF23 filter
- PLUS 100ft extension cord (laying on ground)
- Compared to utility where possible
- FAR quieter measurements discovered.

---
MIF23 Filter
REFERENCE: https://cdn.automationdirect.com/static/manuals/emifilters/MIF23.pdf
“Filter Insertion Loss Characteristics, CISPR 17 – 50 Ohm method”

---
Measurement Locations
Left = 1 Right = 2

---
Final Result
Baseline Measurement

---
Spectrum Analyzer measurements comparison with existing EOC
Power measurements (same antenna) @ 10kHz BW at new EOC site:
3.5MHz -123 dBm
7 MHz -121 – 122.5 dBm
Old EOC roof is 40-50 dB more noisy.
Old EOC Parking Lot is still as much as 30dB more noisy...
To correct to 10kHz bandwidth, subtract 10dB for power measurements.

---
Plotted on RSGB Data dBuV/m
3.5 MHz data seem reasonable, but 7 is at low end of RSGB measurements and 10 MHz much lower.
Suggests AF calibration may be suspect for 10 MHz...so the dBuV/m measurements may need further refinement, but the spectrum analyzer dBm measurements with same antenna, versus older EOC are still quite relevant. .

---
Conclusions
- Making accurate noise measurements is tricky, requires attention to inadvertent corruption due to power system noise in measurement setup
- AF calibration for 7/10 MHz of simple antenna appear suspect.
- New EOC site (when comparing dBm measurement, same antenna) is FAR quieter than built-out existing site.
- When more accurate 7MH/10MHz AF values are available, retained dBm measurements can be re-converted (hence still useful)

---
Next: Improvement Steps
- Improve AF for simple 2-foot antenna by creating individual full size dipoles for 3.5, 7 and 10 MHz – out in large 5-acre back yard
- Place 2-foot antenna at center of full size dipoles for each comparison
- Power either from filtered diesel or long extension cords.
- Solar panel system off.