## Slide 1: All About NXDN
In West Central Florida

## Slide 3: WHAT IS NXDN?
Ultra Narrowband Digital Mode - 6.25 KHz
FDMA Modulation for Clear Audio and Data Streaming
Supports Multiple Talkgroups for Optimal Channel Utilization

## Slide 4: Superior Weak Signal Performance
Decodes digital stream down to -116 dBm
Decodes clear, easy to understand audio when Analog is noise
Optimal for use INSIDE well constructed structures
Works equally well in repeated and simplex modes

## Slide 5: NXDN RADIOS
FIRST Generation since 2005
No Over-The-Air Alias
No Talkgroup Scanning with SELective Squelch
Limited Text Messaging

## Slide 6: NXDN RADIOS
SECOND Generation Radios Since 2015
Supports Over-The-Air-Alias (Transmit your FCC Callsign)
Supports Talkgroup Scanning in SELective Mode (RX Group)
100 character Text Messaging

## Slide 7: ICOM vs JVC-KENWOOD
CONVENTIONAL VOICE COMPATIBILITY
PROPRIETARY TEXT MESSAGING - No Bridge to Translate one format to the other
OTHER PROPRIETARY FEATURES

## Slide 8: WHERE CAN I PURCHASE A NXDN RADIO?
NXDN is a Part 90 Land Mobile Radio Product
ICOM and JVC-Kenwood LMR Dealers are primary suppliers
The Internet
Traditional Amateur Radio Dealers???

## Slide 9: Amateur vs LMR Hardware
AMATEUR
Amateur Frequencies ONLY
Often 430-450 MHz (not the entire band)
Technical Specs not as refined
LMR
Includes ENTIRE Amateur Radio Band
Includes FRS-GMRS Frequencies
Includes Part 90 Band (for EmComm)
Better Technical Specifications means Better Performance
Not prohibitively expensive

## Slide 10: NXDN Radios
Low Split Portables and Mobiles (400-470 MHz)
ICOM F6130D is an ALL BAND Mobile (400-512 MHz)
WBFM Analog Option Available on some radios
All NXDN Radios Can Operate In Analog Mode
After market Antennas Offer Little to No Advantage
Look at Wide-Band Antennas (400-500 MHz)
Multi-polarized and Circular Polarized (CP) offer BEST Performance

## Slide 11: OPERATING TIPS
Announce Yourself with Callsign AND Talkgroup
Use TG 1200 as a Calling TG
Use TG-1 when you are using a Single Repeater
BUSY LOCKOUT

## Slide 12: The ni4ce NXDN Network is Radio Over IP not Voice Over IP

## Slide 13: WEST CENTRAL FLORIDA TALKGROUPS
1 – LOCAL to each Repeater
1200 – FLORIDA
1201 – West Central FL
1215 – SW Florida (S. Sarasota, DeSoto, Charlotte & Lee Co)
1230 to 1233 – TACTICAL On Demand Talkgroups
1299 – NWS Ruskin SKYWARN

## Slide 14: FUTURE ni4ce IMPROVEMENTS
VOTE SCAN (Channel Steering based on RSSI)
A more ROBUST Infrastructure
GPS Signaling Ported to APRS

## Slide 15: NXDN CONTACTS
Paul Toth-NB9X
ptoth1@tampabay.rr.com
Tom Chance-K9XV
k9xv0829@comcast.net