## Slide 1: Direct Calculation of Tuner Losses
Dave Birnbaum
K2LYV

## Slide 2: What, Why
Amateurs are using a huge variety of antennas these days. Many of these need some sort of tuner to provide a good match to a transceiver.
With the availability of fast computers and antenna modeling software (EZNEC, 4nec) many antenna designs can be modeled in detail which includes direct calculation of antenna impedance vs. frequency.
Tuners are very good but not perfect.
  Losses in inductors, voltage limits on capacitors
It could be important to know the frequencies where an antenna could cause failures in the tuner.

## Slide 3: The L-network
In principle any two (complex) impedances can be matched at one frequency by an L-network.
I will limit this discussion to an L network with a capacitor shunt to ground and an inductor in series
  Most (all) autotuners use this configuration
  The analysis can easily be extended to any combination of elements i.e. two capacitors, two inductors, different shunt or series combinations.
Two configurations differing on where the shunt element is

## Slide 4: Solving for element values
First consider circuit A:
We want Zin = 50Ω
Zin =
For match we need the real part of Zin=50 and the imaginary part = 0.
Notice that the only element that can change the resistive part of the antenna to 50 ohms is the shunt capacitor. The function of the series inductor is to cancel any remaining complex component of the parallel antenna-capacitor combination.
Zant=Ra+ j Xa
Zin

## Slide 5: Solution – ideal components
Solving the equations for the apparent impedance gives values for Xc and Xl:
Easier to solve for admittance of capacitor, Bc (Bc = 1/Xc)
  Find value(s) of Bc that make the R component 50 ohms
The value of the series inductor is found by setting Xl to cancel any remaining capacitive reactance:

## Slide 6: We can calculate currents & voltages
Assume some “standard” power – I use 100 W
Iin is easy –
  Notice all input current flows through the inductor in this configuration
  Since effective impedance is 50Ω current is 1.414A
Iin splits between shunt capacitor and antenna:
Iin
Iant
Ic

## Slide 7: Correction for “real” components
Since the components of the matching network are good, i.e. High-Q, we can usually safely assume that adding the resistive parts will not change things very much
  But if series resistive component is more than about 10% of antenna resistance, add series resistive component and re-solve
  Use ideal currents for calculations
  jXc -> Xc/Qc + jXc; jXl -> Xl/Ql+jXl
  Most losses in inductor
  Voltage on capacitor can be a problem
Current Iin splits between capacitor and antenna:
So we have:

## Slide 8: Alternate configuration
Similarly for circuit B:
Again we want Zin=50+j0, so solve for Re(Zin)=50 and Im(Zin)=0
Result:
Note: This can only be used when resistive component of load is ≤ 50Ω
Zin
Zant=Ra+ j Xa

## Slide 9: Calculating currents and voltages
Iin splits between capacitor and inductor + antenna
Adding lossy parts we get:
Iin
Ic
Il=Ia

## Slide 10: Some Examples
Short (18 ft) vertical on 80M
  Za = 17-j1945
  For match L= 89μH, C=809pF
  100 W in, Pinduc=25W, Vc=71V
    Are the toroids in your rig’s antenna tuner big enough to dissipate 25 W?
End fed 45’ wire w/o balun at 10.1 MHz
  Za=334-j572
  For match L=3.96uH, C=39.8pF
  100W in, Pinduc=1.8W, Vc=362V
    Adding 4:1 or 9:1 balun lowers Vc but not much effect on Pinduc
In general, worst case is low Rant and/or high negative (capacitive) Xant.
Note that transmission line between antenna and tuner may transform a not so bad impedance to a “bad” one.

## Slide 11: Implementation
I have implemented the above calculations in a Python program.
  Implementation example rather than finished program – simple U/I etc.
  Can run with manual or read data from file
Why Python?
  Simple language to learn
  Handles complex numbers natively
  Free compiler/IDE
  Large number of free extensions and libraries, e.g. serial control, plotting, much more

## Slide 12: What about the T network?
While most of the autotuners are L-networks, many manual tuners use a T-network configuration (most common is shunt inductor between two series capacitors)
While one can calculate the input impedance presented by any given antenna, finding the “right” setting for the tuner is not simple
  Three variables to solve two equations means that there are multiple settings that will give a match
  Not all settings are equal as far as efficiency e.g. coil losses, capacitor voltages.
  Analytic solution replaced by optimization
    probably to find lowest power loss of settings that give a match.

## Slide 13: Some final comments
If you’re going to model your antenna, model your tuner too.
Consider all combinations of L-networks: two inductors, two capacitors, series capacitor/shunt inductor.
Note that you can run this “backwards:
  If you know values of L network components that give a match, you also know the impedance at the tuner input
    You need to have a way to know values of L,C at each setting
  If the tuner isn’t at the antenna, you can use transmission line equations to correct for intermediate transmission line
  See Belrose QST Sept. 2006, p. 56 H&K note