## Slide 1: No spectrum analyzer? (Maybe) no problem!

## Slide 2: History
I was plagued by a broadband noise source somewhere nearby that had levels around S8-9.
Wanted to look at spectrum on noise over wide band to look for clues as to noise source.
But I don’t have a spectrum analyzer
What to do?

## Slide 3: Solution!
What I do have is a radio controlled by my shack computer
  Computer can set frequency and read S-meter
Write a program: set frequency, read S-meter, and repeat, stepping frequency over the band of interest
Look at output to see if there is a clue to noise source

## Slide 4
Max Freq?
Set initial frequency
Wait 1s, Read S-meter
Step frequency
Step size can be as fine or coarse as you need

## Slide 5: Sample Python program
import serial
import time
import random
#Set up frequencies to monitor
# cover all bands
freqstr = ("03613000", "07112000", "10113000", "14113000", "18113000", "21113000", "24913000", "28113000")
ser = serial.Serial(0, baudrate = 38400, timeout = 1)
outfil = open('Noise.dat',"w")
while True:
starttime = time.time()
i = random.randint(0,6)
freqset = "FA"+freqstr[i] + ";"
ser.write(freqset)
print starttime
while time.time() - starttime < 300.0:
print time.time() - starttime
ser.write('SM0;')
reading = ser.read(8)
ctime = time.strftime("%H:%M:%S ")
ostring = freqset + ctime + reading +"\n"
outfil.write(ostring)
print(ostring)
time.sleep(15)
outfil.close()
exit()

## Slide 6: Different options
Sample frequency at random over some range
  Results in broad coverage more rapidly, lessens chance of hitting “real signal”
Sample frequency over smaller range with smaller step
  Fine resolution limited by receiver filter

## Slide 7: 40 meters at 10kHz steps
Chart: 

## Slide 8: Random sampling 2-30 MHz
Chart: S-meter reading vs Frequency taken 5/24/14

## Slide 9: What else?
What else can we do with the combination of computer controlled rig and computer?
  Could get higher resolution by using audio output of rig and FFT
  Your ideas??