Introduction to the
PICAXE Microcontroller
By Darrell Davis KT4WX
ARRL Technical Specialist
ARRL West Central Florida Section

---
KEY TO THIS PROGRAM
If you like this program:
Fall asleep with your head forward
If you dislike this program:
Fall asleep with your head backward.
All the heads should be forward
 when I am finished :-)

---
PROGRAM OUTLINE
I. History of the PICAXE
II. PICAXE Processor Line
III. PICAXE Commands
IV. PICAXE Programming
V. PICAXE Sample Program
VI. PICAXE Resources

---
I. History of the PICAXE
Based upon the Microchip PIC Series
of Microcontrollers.
PICAXE is a pre-loaded “Basic Interpreter”
or “bootstrap firmware code”.

---
I. History of the PICAXE
Produced by a UK (British) company called
Revolution Education Ltd. (Rev-Ed)
The first PICAXE interpreter was produced
in 1999 but has been vastly improved and
expanded since that time.

---
II. PICAXE Processor Line
Currently there is a wide selection of
processors available in the PICAXE line.
Available in 8 Pin to 40 Pin DIP packages.
Available also in Surface Mount:
(SOIC, and TQFP Packages).

---
II. PICAXE Processor Line
PICAXE M2 SERIES
 Standard Series of Controllers
Processor	Program Memory	I/O Pins	RAM	Clock
PICAXE 08M2	2048 Bytes (2K)	6	128 Bytes	4-32 MHz
PICAXE 14M2	2048 Bytes (2K)	12	512 Bytes	4-32 MHz
PICAXE 18M2	2049 Bytes (2K)	16	256 Bytes	4-32 MHz
PICAXE 20M2	2048 Bytes (2K)	18	512 Bytes	4-32 MHz

---
II. PICAXE Processor Line
PICAXE X2 SERIES
Advance Series of Controllers
More Features, Ports, and Speed
Processor	Program Memory	I/O Pins	RAM	Clock
PICAXE 20X2	4096 Bytes (4K)	18	256	4-64 MHz
PICAXE 28X2	4096 Bytes (4K)	22	1280	4-64 MHz
PICAXE 40X2	4096 Bytes (4K)	33	1280	4-64 MHz

---
II. PICAXE Processor Line
PICAXE 08M2
PICAXE 14M2

---
II. PICAXE Processor Line
PICAXE 18M2
PICAXE 20M2

---
II. PICAXE Processor Line
PICAXE 20X2
PICAXE 28X2

---
II. PICAXE Processor Line
PICAXE 40X2 – TOP OF THE LINE
600 mm DIP Package – All others 300mm DIP Package

---
II. PICAXE Processor Line
PICAXE 08M2
MODULE
PICAXE 28X2
MODULE

---
III. PICAXE Commands
Originally, microcontrollers were
programmed in assembler
More recently, nearly all microcontroller
programming is done in C++
The PICAXE is programmed in BASIC!!

---
III. PICAXE Commands
Digital Input/Output Commands
COMMAND	DETAILS	COMMAND	DETAILS
High	Switch an output pin on	Pwmout	Generate a continuous pulse width modulation
Low	Switch an output pin off	Pwmduty	Set duty cycle of a pulse width modulation output
Toggle	Switch an output between on and off	Input	Set a pin as in input
Sound	Generate simple sounds	Output	Set a pin as an output
Button	Detect and debounce a pushbutton switch	If Pin	Respond to the state of an input pin

---
III. PICAXE Commands
Time Delays and Variables
COMMAND	DETAILS	COMMAND	DETAILS
Pause	Pause for a defined number of milliseconds	For/Next	Repeat a loop for number of time. Return from loop
Pauseus	Pause for a defined number of mcroseconds	If / Else	Conditionally execute program code. Alternative
Wait	Delay for a number of seconds	EndIf	End of If / Else statement
Sleep	Sleep for a period of time	Gosub / / Return	Call a routine Come back from routine
Doze	Reduce pwr consumed for a short period of time	Goto	Continue program execution from label

---
IV. PICAXE Programming
PICAXE is programmed with a serial connection
Programming Pins: SERIN, SEROUT, GND.
Programming can be done with a Windows
Based PC with a RS232 Serial or USB Port.

---
IV. PICAXE Programming
Serial Port Programming
Can use a DB-9 Male in Place of 3.5 mm Connector

---
IV. PICAXE Programming
USB Port Programming
Uses a USB to Serial Adapter.
USB Serial Cable
#AXE027
USB Serial Adapter
#AXE029

---
IV. PICAXE Programming
Programming Software:
PICAXE Programming Editor – Version 5

---
IV. PICAXE Programming
Programming Software:
PICAXE Editor 6
(Replaces PICAXE Programming Editor V5)

---
IV. PICAXE Programming
Programming Software:
AXEPAD: Available in Windows, Linux, and Mac

---
IV. PICAXE Programming
Items needed to start with
PICAXE Programming and Experimenting:
Computer with Windows, Linux, or Mac OS.
More programming applications available with Windows.
Serial Cable or USB to Serial Converter:
If computer has USB Ports only or if desired Port.

---
IV. PICAXE Programming
Items needed to start with
PICAXE Programming and Experimenting:
3VDC TO 5VDC Power Supply or Battery.
DO NOT EXCEED 5VDC.
PICAXE Controller of choice.
Solderless Breadboard with parts needed to breadboard desired circuit..

---
IV. PICAXE Programming
Do not apply more than 5VDC to your PICAXE!!

---
V. PICAXE Sample Program
Quick Program: BLINKNG LED
Turns Port 4 (PIN 3) On and off in a continuous loop.

---
VI. Sample PICAXE Project
DEMONSTRATION TIME:
A 3 minute or 10 minute timer with a PICAXE 08M2
Processor with less parts count than a comparable
   555 Timer.
The 555 Timer cannot do 2 time modes without
 a higher parts count.

---
VI. PICAXE Resources
BOOK RESOURCES:
Ham Radio for Arduino and PICAXE
by Leigh L. Klotz Jr. WA5ZNU
ISBN-13: 978-0872593244
Programming and Customizing the PICAXE
Microcontrollers by David Lincoln
ISBN-13: 978-0071457651

---
VI. PICAXE Resources
INTERNET RESOURCES:
PICAXE Website: http://www.picaxe.com
PICAXE Programming Software:
   http://www.picaxe.com/Software
PICAXE Hardware Manuals:
 http://www.picaxe.com/Getting-Started/PICAXE-Manuals/

---
VI. PICAXE Resources
INTERNET RESOURCES:
PICAXE Wikipedia Page:
   http://en.wikipedia.org/wiki/PICAXE
YouTube Video Tutorials:
https://www.youtube.com/user/azadude18/videos

---
CONTACT INFORMATION
Darrell Davis KT4WX
6350 Mills Road
Fort Meade, FL 33841-9584
(863) 245-9923
Email: kt4wx@arrl.net
Website: http://www.kt4wx.org