Poor-Man’s SATELLITE STATION
The story of trying to develop an inexpensive ground station to use amateur radio satellites
Gordon Gibby KX4Z

---
Categories
- FM Satellites – powerful, “easy” but terribly over crowded
- Linear Satellites – appear weaker, but much more bandwidth
- Lots of PROBLEMS compared to normal ham QSO...

---
Many Hurdles
POINTING
    - Satellite is MOVING TARGET (orbits also change…)
    - Getting rotator to work
    - Controlling rotator
FREQUENCY
    - Constantly changing Uplink Doppler Shift
    - Constantly changing Downlink Doppler Shift
    - “Finding Yourself” (Offsets & Full Duplex)
1. TRANSMIT POWER (antenna)
2. RECEIVER PERFORMANCE (antenna/preamp)

---
Initial Question: Transverter?
- No VHF/UHF linear transceiver @ start
- 5-10 W transverters available (Ukraine)
- Sbitx transceiver / 7300
- Seemed like too little power….

---
Transverter
Various models have input attenuators (or none) so attention has to be given to avoiding destroying the input with a transmitter.
Often they have “auto PTT” – but you may need much more precise result, so adding an external connection may be required.

---
1. POINTING:
a) Rotator Controllers
- Previously a separate hardware item that received commands from trig-based software and drove the rotator to point
- CSN S.A.T. combines software and controller to drive Yaesu rotators
- Now can be done much less expensively in software/micro controllers also
https://www.nf4rc.club/how-to-docs/satellite-system-part-i-overview/

---
Traditional ($$$$) Rotator Control
CSN solution drives
Rotator directly

---
K3NG (pennies) Rotator Controller

---
My K3NG-based Nano Controller

---
Gerbers for PCB
- Control via USB port (Yaesu language) or manual
- Analog potentiometer angle sense inputs
- DC output controls for Yaesu DC motor rotators
- LCD monitor output reads position
Shared Project on PCBWAY
https://www.pcbway.com/project/shareproject/K3NG_Rotator_Dual_Axis_Controller_Board_fd759cc2.html
https://www.nf4rc.club/how-to-docs/satellite-system-part-ii-rotator-control-board/

---
POINTING:
b) Control Software: Gpredict
Nice display
TLE updates
Controls rotator via HAMLIB
Controls simple radio(s) via HAMLIB
FREE
HAMLIB: rigctld to control rig
HAMLIB rotctld to control rotator (can speak YAESU)
I got it working with the rotator,
But I could NEVER get it to properly control the ICOM 820H to link uplink and downlink with changes

---
Software: SATPC32
- Properly controls ICOM transceiver (CI-V)
- DDE output to control rotators
- 3rd party WiSP reads DDE and controls Yaesu-type rotators

---
POINTING:
c) Hardware: Yaesu Dual Axis Rotator
- $$$700+
- Basically G450 azimuthal rotator
- Combined with elevation rotator

---
Homebrew Elevation Rotator 1.0
90 degree gear-based rotator
My first effort with linear actuator
Clueless about connecting rods, diameters etc
WORKED...but shaky
https://www.nf4rc.club/how-to-docs/satellite-system-part-iii-antenna-dual-axis-rotator-system/

---
Dual Axis Rotator/Antenna 1.0
Actually worked and made a contact with it!

---
UPGRADE!
Elevation Rotator 2.0
- Build around much stronger aluminum masts
- Utilize longer linear actuator (12V DC motor)
- Simple potentiometer angular monitoring
- 3D print as many parts as possible, so design is immediately repeatable by other interested hams

---
Elevation Rotator 2.0
3D Printed Rotator Components
2’ /Amazon aluminum azimuthal boom
1.5” Amazon alum. Elevation boom
Amazon 6” linear actuator
Bushings to support elevation boom
Geared control arms (two)
Geared potentiometer arm
Potentiometer support
Limit Switch support
Limit Switch actuator
Pin for linear actuator
Easy to replicate by anyone!!

---
2. Frequency Control
- GPREDICT via rigctld can control simpler radios….
- SATPC32 – finally able to control both MAIN and SUB of Icom 820H (and subsequent transceivers)
- CI-V open collector control via USB laptop output with cable
- 820H lacks SPECTRUM DISPLAY
- Finding self much easier with spectral display – sBitx with Transverter!

---
Frequency Issues
- Beyond separate uplink and downlink Doppler errors…
- Satellite offset may DRIFT
- My transceiver frequencies also DRIFT
- FINDING YOURSELF NOT EASY!!
- Spectral display helps a TON
- 820H doesn’t include….
- Sbitx Does

---
Transverter to the Rescue?
- Split the received signal –> TWO receivers
  - Portion to 820H
  - Portion to Transverter → 10meter sBitx
- Problem: Add transverter and sBitx drift now!!
- Must track commands to 820H and command sBitx to equivalent frequency….
- Wrote c-code on Rasp. Pi to translate and feed the sBitx with commands – allows corrections for offsets; finding self much easier
  - Code allows me to make corrections for frequency errors on transverter+sBitx to math the 820H

---
A Fairly Complicated Setup
- Trying to keep all of it straight
- Blew up 2 (less expensive) preamps in the process
- Made a CW QSO on RS44 Russian satellite

---
3. Transmitter Power

---
Used ICOM 820H
- Low cost duplex VHF/UHF radio
- 40W typical output
- Possibly good sensitivity

---
Antenna Gain
- Problem of Circular Polarization
- Pairing two orthogonal Yagi's
- 3dB loss due to pairing
- Difficulties of matching!
- Typical solution: 50 ohm → ¼ match to 100 ohm, THEN parallel

---
Homebrew 2meter / 70 cm antennas
- Difficulties with Aluminum Arrow Shafts
- Arrow inserts
- Threaded Rods
- J driven elements vs. folded dipole
- Matching problems…..
- Lack of experience with better matching systems

---
Ken Britian WA5JVB 1994
http://www.fredspinner.com/W0FMS/CheapYagi/vjbcy.html

---
My attempt

---
Lots of Trouble with J Driven Element / Matching
https://www.nf4rc.club/how-to-docs/satellite-system-part-iv-cross-polarized-yagis/

---
Good isolation between antennas

---
Less than exciting gain measurements when compared with standard dipoles in my backyard antenna range….

---
Commercial 70cm Yagi
- Far better machining
- Gamma Match (Teflon?)
- Need non-conductive support boom material to mount on….

---
3. Receiver Sensitivity
(and allowing spectral display)
- Coax run adds loss
- Attempting to split receiver signal adds loss
- Uncertain 820H receiver gain/sensitivity

---
Preamplifiers
$376++ preamp with relay switching included; versus $16 preamp without relay switching...

---
Preamp Control
- Standard: +V on coax center conductor during receive enables preamp
- 820H allows pre-setting of which BAND will have +V on receive (VHF= SO-239; UHF = N)
- Does NOT prevent RF Transmit from switching to unexpected connector!! Making +V critical to protection.

---
Sequencer / ALC Pwr Level

---
Sequencer Works!

---
2meter Preamp Relay

---
2meter Preamp Relay Board
https://www.nf4rc.club/how-to-docs/satellite-mast-mounted-preamp-protection-board/

---
Inadequate UHF Isolation
- Good to have 15 dB more isolation than GAIN! (prevent oscillation)
- Isolation between preamp coaxial connectors and transmit pathway (1MHz-2.1 GHz) -- both input and output are similar. This shows the isolation of the preamp from the transmit pathway at two meters is approximately 36dB, but the isolation declines markedly at higher frequencies.
- LPF required to prevent oscillation.

---
UHF Preamp Switching -1

---
UHF Relay Switching

---
UHF PreampSwitcher

---
UHF Relay Design
- Required special relays
- Microstrip design (needed wider traces)
- Thru SWR < 1.3:1 thru 70cm
- Bias-Tee requires dual-stage LPF to avoid false triggering

---
Finding Myself:
Attempt to Monitor with Sbitx
- ICOM has no spectral display
- Sbitx on 10meters / transverter
- Feed both from receive antenna ( may require preamp or else effective noise figure gets much worse….)

---
SATPC32 correctly controls 820H
- Able to correctly adjust both receiver and transmitter frequencies
- Doppler control
- Able to adjust separately to correct for satellite offset drift/ground station drift

---
Control sBitx
- Sbitx includes HAMLIB type tcp/ip control of frequency (SATPC32 can’t speak)
- Wrote Raspberry Pi software to monitor CI-V commands to ICOM; offset properly for sBitx/transverter; interface to sBitx software.
- Includes adjustments for drift

---
Where Next?
- Improve / Stabilize Yagi’s
- Finish dual axis hardware / sleeve mount non conductive boom (1” ID PVC) – VALIDATE DESIGN
- (Publish .STL files and other updates)
- Install Sequencer
- Install Preamp(s)
- Track Satellites on RECEIVE
- Test Transmitting – Validate designs!
- Find my signals! (Hopefully stronger!)
- WORK STATIONS!!

---
Questions, Comments?