## Slide 1
KV0OOM (aka Mike)
RETIRED = Looking for a new hobby because 11 is not enuff.
Technician + General on 18 Nov 2015
Extra on 08 Jan 2016
Not that smart, 5 years as a classroom instructor for electronics.

## Slide 2
NOTE:
If you fall asleep during this presentation, that is okay. It will be my fault for being boring and you will not be punished.

## Slide 3
When I first learned programming, I did not wonder what a program can do. I was at a loss for thinking what I wanted a program to do. Then I finally figured it out: To make repeating tasks easy.
What is a "repeating task" you ask? You didn't, really? Okay, but I am going to tell you anyhow. It is something you have to do more than twice, like take out the garbage. Wow, if we could only make the computer do that!
Robots on the assembly line are a prime example of repetitive tasks. Simple or complex, it is a series of repeating operations.

## Slide 4
Several TechCons back, I presented a project where I built a rotor control box, using a Picaxe 08M2 controller, for my Hy-Gain rotor. I had a perfectly good control box, so did I need a fancy version that does the same thing? Where is the repeating task in this?
The intent was to automate the repeating task of trying to point the antenna in a desired direction. Yes, I had to turn a knob to set the direction, just like the original controller, but I could pre-set the direction while still in a QSO. Then push a button and off it goes (contester delight). It automatically accelerates, rotates, decelerates, and coasts to (or brakes at) the desired position.

## Slide 5
This should demonstrate knowing programming can be useful.
"But I do not know how to program!", you say? No worry, Blockly is your friend. If you ARE a programmer, Blockly can help you to transition to BASIC for the Picaxe and other BASIC-capable processors.
Blockly uses visual blocks that link together to make writing code easier, and can generate code in various languages. It can be customized to generate code in any textual programming language. Which is what Revolution Education did for the Picaxe family of microcontrollers. So, where do we start?

## Slide 6: You start with an idea or a project you read about somewhere. The focus today will be on the idea launch. I used to hate block diagrams, but now they are my friend. Put your idea or plan on paper using blocks to represent actions to be performed. Any graphics program that can draw lines, boxes, circles and allow text to be added will work. My personal favorite is MS Visio, although the Picaxe Editor has Logicator built in.

## Slide 7: However, we must put first things first. You likely have the circuit diagram for a Picaxe project in mind. Before you can create the software, we must develop the hardware. To help, we shall start with Pebble first. Pebble allows you to "build" a project on a virtual solderless breadboard. In other words, we will copy the electrical schematic to a mechanical components placement design. (Short version) Install all your components on the breadboard and hook everything up. I discovered this is easier to do rather than try to do it on an actual breadboard.
So, you might have a project like this one…

## Slide 9: And end up with something like this (obviously from a different schematic)… Triple-check everything and then copy the layout to the real breadboard.

## Slide 10
Because you have all the chip pins identified, you can begin writing or creating the program, almost. We will shortly open up Blockly and go to work.
But first, a brief side bar (explanation) on saving your Pebble work…
About 2/3 of the way down the Pebble side panel is a button labeled “Save or Load”. Clicking that will open a window with this message at the top:
To Save : Copy and paste all text below into a text editor and save it. To Load : Paste previously saved text into this text area and click 'Load Circuit'.
Unlike most other programs, file input-output is a copy/paste operation. This means, don’t forget to copy your work and paste it in a text file.

## Slide 11
If you are using Blockly, and you created a functional block diagram, your project will be halfway done. As you build your Blockly diagram, refer to the material you have already created.

## Slide 12: Moment of Clarity
To be completely honest, you should know SOMETHING about programming. This is not the same as knowing how to program. Programming is basically conditions,
decisions, and actions.
Remember hearing this as a kid, “If you don’t pick up your toys, then I will put them in the garbage.” You action was based on a conditional decision (toy box or garbage can).
This is programming.

## Slide 13: And so is this…

## Slide 14
If you want to turn a light on, you don't need a program for that. Just walk over and turn the light on.
If you want to turn a light on when you enter the room, that you can program. Use an ultrasonic motion detector to get the job done.
But if you come in and sit down, the motion detector will not see motion and will turn the light off.
So.... you add an infrared (IR) sensor to detect your body heat. That can be used to keep the light on.

## Slide 15
The graphic a couple of frames back is a bit hard to read, so here it is in plain English:
At the program start, DO
IF input C.1 is ON
THEN Turn output B.0 ON and add 1 to varA
ELSE Turn output B.0 OFF and reduce varA by 1
MAIN:
Do
If C.1 = 1 Then ;The button is pressed
Set B.0 = 1 ;Turn on the LED
varA = varA + 1 ;Add 1 to the counter
Else
Set B.0 = 0 ;Turn the LED off
varA = varA – 1 ;Subtract 1 from the count
Endif
Loop ;Repeat

## Slide 16: Block Diagram

## Slide 17: Functional Layout

## Slide 18
Now we see how Blockly does it…

## Slide 20
main:
do while pinB.1 = 1
if pinB.2 = 1 then
high C.1
pause 1000
low C.1
high B.3
else
toggle C.1
pause 500
toggle C.1
low B.3
endif
loop
stop

## Slide 21
Let’s Go Step by Step
Like building a house, we start with the outside framework first and work inwards. Select the controller type.

## Slide 22
Outside Loop Added
Added
Docked

## Slide 23
Inside the repeating loop, we add the decision (Variables) section.

## Slide 24
Adjust for the correct location.
When added, it will automatically dock.
Hover over the block, and a hand will appear. Use that to move the block to the correct location.

## Slide 25
OOPs!!! The wrong If-Then-Else.
We should have chosen from the INPUT list, instead from the VARIABLES list. No worry, an easy fix.

## Slide 26
Continue by adding the Decision actions
We are almost done…

## Slide 27
Now update all the variables as needed.

## Slide 28
View Your Work in Code
You will copy this text and paste it into the Picaxe IDE. At this point, you have not needed to write a single line of BASIC code. If the program does not work as you expected, simply come back into Blockly and fix it.
Do not forget to do a File, Save As to save your Blockly work.

## Slide 29: C O M M E N T S : Blocky is XML only. There is no import (no XML form for the graphics) for text files or source code. However, you can view the source code it creates. You can copy the unformatted PICAXE BASIC to a text file and use that. I suppose by now you are seeing the limitations of free software, where you are expected to do some of the work yourself. But you have to admit Blockly, Pebble, and even the Picaxe Editor v6, are pretty amazing considering they are provided for a $3.oo chip and cost nothing.

## Slide 30: Youtube Videos
https://youtu.be/dtjDL3fjEqo
https://youtu.be/6W1G9K7Ry_I
https://youtu.be/4emX7GIyTwg

## Slide 31: Resources
Several documents that can be downloaded are included with the files of this presentation…
Picaxe (Blocky) Manual5.pdf
Logicator Guide.pdf (Now included in the Picaxe IDE)
BLOCKLY was developed by Google, so GOOGLE it!

## Slide 32: KV0OOM
This project was initiated by knowing not every Ham is a programmer, but should still be able to have fun with the Picaxe family of microcontrollers.
kv0oom, Amateur Extra.
kv0oom.extra@gmail.com
Old, but not an Old Timer.
Google is your best friend.
RETIRED and hobby poor!