## Slide 1: PEBBLE
Picaxe Electronic Bread Board Layout Emulator
Presented By
Mike Hembrey
kv0oom

## Slide 2: Solderless Breadboard

## Slide 3: What It Is
A solderless breadboard is primarily used for rapid prototyping and testing of electronic circuits before committing to a permanent design on a printed circuit board (PCB), allowing users to easily build, modify, and experiment with different component arrangements without the need for soldering, making it ideal for beginners and hobbyists to learn about electronics and test circuit concepts quickly.

## Slide 4: Key Uses
Circuit prototyping:
Quickly build and test different circuit designs with various components like resistors, capacitors, transistors, and integrated circuits (ICs) before finalizing the design on a PCB.
Learning electronics:
Due to the ease of use and ability to quickly change connections, breadboards are excellent for beginners to learn about basic electronic components and how circuits work.
Troubleshooting circuits:
Identify issues within a circuit by easily rearranging components and checking connections on the breadboard.
Testing new components:
Experiment with new electronic components without having to solder them permanently to a circuit board.
Developing sensor interfaces:
Test how different sensors interact with a microcontroller or other electronic systems by connecting them to a breadboard.

## Slide 5: Key Uses (more)
Building temporary setups:
Create temporary circuits for demonstrations, experiments, or quick testing of functionality.
Important points to remember about solderless breadboards:
Not for permanent circuits:
While you can build functional circuits on a breadboard, it is not designed for long-term use due to the potential for loose connections over time.
Power rails:
Most breadboards have dedicated power rails (usually marked red for positive and blue for ground) that run along the edges, simplifying power distribution to different components.
Connection points:
Components are connected by inserting their leads into the holes on the breadboard, where conductive strips underneath create connections between specific rows and columns.

## Slide 6: PEBBLES Application
Not limited to just Picaxe projects
Handy for adjusting layout of parts
Easy to design modules for reuse
Screen capture for presentations
1 to 1 transfer to PCB with solderless pattern

## Slide 7: Not limited to just Picaxe projects
This is the beginning of a 555 timer project. The black line outlines a ½ breadboard ready-made PCB.

## Slide 8: Radio Shack not all bad!

## Slide 9: Solderless and Solder Boards

## Slide 10: Signal to UFO

## Slide 11: Make it a reusable module, but…

## Slide 12: These 2 resistors must be in the Picaxe circuit.

## Slide 13: Solar Tracker

## Slide 14: Select the Solderless Layout (50 rows, 2 parallel rails, red at top)

## Slide 15: Many IC Choices Available (Not just for Picaxe circuits)

## Slide 16: Simple Strobe Circuit

## Slide 17: 08M2 or 14M2, Same Code (Pin assignments will be different)

## Slide 18: Place Big Stuff First

## Slide 19: Now Add the Smaller Parts

## Slide 20: Finally, Add the Jumpers

## Slide 21: Save your work!!!
The PEBBLE application is browser based, so the usual file save and load methods do not apply.
Click on the Save or Load button and a window full of gobbledygook will appear. It actually makes sense if you stare at it long enough.
That text must be copied to a text file and saved so you can find it later.
When you close the browser, your long and hard work is not saved.
Ask about the OOPs.!
To Reload Your Work
Open the saved text file and copy the contents.
Open PEBBLE and click on the Save or Load button.
Paste the contents you copied from the text file (overwrite any existing text).
Click on the Load Circuit button at the bottom on the window.

## Slide 22: Connect the Picaxe Program Cable AXE026

## Slide 23: Apply power to the rails and program using the Free Picaxe IDE
' programmable strobe flashlight
' 10 2006 by Medcosm, LLC
'
' originally created to see if it worked well looking at individual drops of water
' coming out of a faucet, a la the "Time Fountain"
' can use 2 LEDs hooked up to 2 output pins gives more current and brighter light
'
'
' Use this prog w/ Simple Digital Strobe V2 circuit
'
'hardware hookups for this project
symbol LED1=1 'LED1
symbol LED2=2 'LED2 use 2 LEDs for more bightness
symbol BUTN1=pin3 'N.O. pushbutton 1
symbol BUTN2=pin4 'N.O. pushbutton 2
'declare variable space
symbol mode=b0 'mode
symbol curstep=w2 'step size
symbol LEDoffTime=w3 'pause delay
symbol buttonCount=w4 'count how many cycles button pressed
symbol var1=b10 'local variable
symbol var2=b11 'local variable
symbol devcnt=w6 'counts how long device is off
'static vars
symbol LEDpulseval=120 'brightness of LED during pulse mode
symbol devoffcnt=60 'how often to flash when off? 30/.576, approx 30 seconds

## Slide 24: Run your program!
This example circuit simply strobes something using reciprocal or rotary motion. In other words, it makes it look like it is standing still.
Our layout did go past 30 rows, so we could transfer it directly to a ½ solder board copy of the solderless design.
With the source code, you can add features like a potentiometer to replace the buttons for setting the blink rate,
With pins left over, you could add other devices, like a temperature sensor.
You could upsize to a larger Picaxe controller with more I/O pins and add a digital display of the pulse rate.
Yes, you can purchase ready-made strobes on Amazon, but where is the fun in that?

## Slide 25: Useful Links
Picaxe IDE, Blockly for Picaxe, AXEpad, Picaxe VSM: https://picaxe.com/software/picaxe/
PEBBLE Software: https://picaxe.com/software/third-party/pebble/
Picaxe Software Drivers: https://picaxe.com/software/drivers/
Picaxe Manuals for Download: https://picaxe.com/getting-started/picaxe-manuals/
Picaxe Getting Started Tutorial: https://picaxe.com/getting-started/downloading-your-first-program/

## Slide 26: Not a Programmer?
But you would like to play with the Picaxe controllers? Then investigate the BLOCKLY (not a typo) application. Using the same decision making logic you use every day, you can generate working BASIC code for the Picaxe family of chips.

## Slide 27: The Beginning…
Mike Hembrey
Kv0oom
For me, electronics is not job or hobby, it is a religion.
Thank you for attending this presentation.